PicoTCP – Usage and platform integration

# Requirements and Configuration

PicoTCP is designed to be portable and versatile. Modules can be activated at compile-time, or excluded from the compilation in order to reduce the build size, or to save resources at runtime. This characteristic allows an embedded application to create different types of appliances, starting from a small forwarding multi-protocol switch, to fully-featured TCP hosts, supporting internal applets as well as generic POSIX-compliant socket interfaces.
###### Supported features

###### Module dependencies

###### Target requirements
PicoTCP can run on several different hardware architectures, and can be integrated with virtually any operating system, or within a standalone application. It is possible to run PicoTCP on big-endian as well as little-endian CPU configurations. PicoTCP uses gcc-specific tags that may not be compatible with other compilers. The amount of resources needed may vary depending on the modules that are compiled-in. However, adapting to a specific hardware platform or for a particular use may require some integration effort.
###### The pico_config.h file
The configuration for all the modules and their features is located in a the pico_config.h file. The files has two sections: “user configuration” and “architecture specific”. The first one is used to enable features to include. Uncommenting a line starting with a “#define” statement will enable the feature described in the comment. The pico_config file is located under the “/include” directory. The second section is used to include the specific implementation of the system interface required by PicoTCP to run on the target as described in the next section. As an example, some architecture implementations are provided:
- a virtual posix target that allows the stack to be run on top of a POSIX compliant operating system (like Linux or other unix-like implementations).
- Arm M3/M4 Cortex board support
The architecture-specific configuration is located in the “/include/arch” directory.

# Porting to a target system
PicoTCP relies on a simple set of system-specific calls that must be implemented externally from the target. Briefly, the interface needed for the stack to run is composed by:
- A mechanism to allocate dynamic memory on the system
- A stable time-source to update its internal counters
For the memory allocation interface, two symbols have to be defined by the system:
- void *pico_zalloc(int size) – (memory allocation)
- void pico_free(void *ptr) – (memory release)
pico_zalloc Must allocate an object of the given size size in memory and set the content of the allocated memory to zero. A pointer to the address 0 will indicate an allocation failure.
pico_free Must must release the memory assigned to the object previously allocated at the address ptr.

For the time keeping, the following objects must be defined by the system:
- static inline unsigned long PICO_TIME(void) – returns current time expressed in seconds
- static inline unsigned long PICO_TIME_MS(void) – returns current time expressed in milliseconds
- static inline void PICO_IDLE(void) – sleep between two consecutive iterations inside the main protocol loop (e.g. to yield the CPU to some other functionality on the sytem)

Finally, whenever debug informations are needed, the system will have to provide a dbg() function that accepts the same variadic arguments model as a standard printf().

# Network devices integration
Every device driver must define its own interface to communicate with the stack. This interface is accessed via the pico_device structure. Every device implements an instance of this structure by populating the following mandatory fields:
- overhead – A positive integer indicating the amount of bytes required by the device driver to implement its header. This is used whenever a network layer allocates a new packet to be sent through this device. If a valued is specified here, it will be possible for the device to seek back in the frame scheduled for sending, and subsequently copy any header information in front of it. Devices dealing with pure stack frames or subparts of it (e.g. Ethernet) should have overhead set to 0.
- The callback send – must be a pointer to a function internally defined in the device driver module. This function will be called every time a frame must be injected in the network. The module can implement a generic send function for all the registered devices, as the device field will be passed as the first argument. The callback prototype is the following:
    int (*send)(struct pico_device *self, void *buf, int len);
  If the device can immediately inject the frame at address “buf” of len “len”, it returns back to the caller the length of the frame injected. If the device is currently busy, this function can safely return 0, and the stack will retry the same operation again later.
- The callback poll – must be a pointer to a function internally defined in the device driver module. This function will be called periodically by the stack, to request a synchronization on the incoming frames. The prototype is the following:
    int (*poll)(struct pico_device *self, int loop_score);
  The poll function must check if the device is ready to receive frames, and for each frame that is directed to the stack, it will call the library function pico_stack_recv(). This function will deliver the received frame to the stack.
  The loop_score variable represents the maximum amount of frames that the stack can process during this call, i.e. the maximum amount of calls to pico_stack_recv() that can be performed during this iterations. The device driver should loop around the packet delivery operation and decrease the loop_score by one every time a frame is delivered to the stack. If during the iteration all the score was used, poll will return 0.
  NOTE: The poll function must return immediately and must never block on hardware-specific operations. If the device is interrupt-driven, the integration will have to provide a mechanism to defer the reception until the next call back to poll. Calling pico_stack_recv() is only allowed from inside the poll() callback, thus a two-halves interface interrupt management design is required, and any memory structure shared between the two halves must be protected against concurrent access accordingly.
- The callback destroy – a pointer to a function that deallocates the device structure itself and frees all the eventual structures allocated by the driver during device creation.

A device driver will have a simple two-functions library API exported in a header file using the same name, in the modules directory. The two functions to export will be:
A create function, accepting any argument required for the internal device configuration, that returns a pointer to the newly allocated device. The function must allocate the device and finally call the library function pico_device_init() in order to register the device into the stack.
The pico_device_init function accepts the following arguments:
    - the device allocated just before
    - a null-terminated string containing a unique device name for the device to be inserted in the system (e.g. “eth0”)
    - A pointer to an Ethernet address in the form of a previously allocated pico_ethdev structure, containing the hardware address to be used by the stack for datalink addressing. If no hardware-specific address is provided to pico_device_init() is provided (i.e. a NULL pointer is passed), the newly created device will be directly attached to the network layer and it will have to provide and process valid IP packets with no further encapsulation.
A destroy routine, accepting the previously allocated device pointer to free all the associated structures.
The way to expand the device driver interface is by simply creating a new specific structure that contains it, so it inherits all the capabilities of the standard structure but also holds the required hardware-specific information. The three callbacks will always receive a pointer to the beginning of the pico_device structure, but the memory area that follows the structure can be used to keep track of the device hardware-specific context.
Naming convention must be followed for the two functions exposed to the user interface to create and destroy the device. The functions must be named pico_X_create() and pico_X_destroy(), where X is the unique name of the device driver.
As an example of a very simple device driver, directly attached to the networking layer using the valid naming convention for the send/poll/create/destroy interface is contained in the source file modules/pico_dev_null.c and its header modules/pico_dev_null.h.

# Socket call function manual

Open socket
Open socket
Server
Client
Bind
Listen
Accept
Send
Recv
Recv
Send
Close
Close
Connect

Figure 1: Schematic overview of a client-server communication sequence
The pico_socket_open function
Description:
This function will be called to open a socket from the application level.
Function prototype:
struct pico_socket *pico_socket_open(uint16_t net, uint16_t proto, void (*wakeup)(uint16_t ev, struct pico_socket *s));
Parameters:
@ net	– Network protocol
PICO_PROTO_IPV4 = 0
PICO_PROTO_IPV6 = 41
@ proto	– Transport protocol [1]
[1] Maybe this should be trans instead of proto ?
PICO_PROTO_TCP 6
PICO_PROTO_UDP 17
@ wakeup	– Callback function that accepts 2 parameters
@@ ev	– Events that apply to that specific socket
 @@ s	– Pointer to a socket of type struct pico_socket
Return value:
“struct pico_socket * ” – returns a pointer to the declared socket , if the return value is “NULL” the socket is not created
Example:
sk_tcp = pico_socket_open(PICO_PROTO_IPV4, PICO_PROTO_TCP, &wakeup);
The pico_socket_read function
Description:
This function will be called to read a string from a socket from the application level. The function checks whether or not the socket is bound.
Function prototype:
int pico_socket_read(struct pico_socket *s, void *buf, int len);
Parameters:
@ s	– pointer to socket of type “struct pico_socket”
@ buf	– void pointer to the start of a string buffer where the string will be stored
@ len	– length of the string that was read from the socket (in bytes)
Return value:
“int” – returns integer representing the number of bytes read
Example:
bytesRead = pico_socket_read(sk_tcp, buffer, bufferLength);

The pico_socket_write function
Description:
This function will be called to write a string to a socket from the application level. This function also checks if the socket is bound, connected and that it isn't shutdown locally. This is the preferred function to use when writing strings from application level.
Function prototype:
int pico_socket_write(struct pico_socket *s, void *buf, int len);

Parameters:
@ s	– pointer to socket of type “struct pico_socket”
@ buf	– void pointer to the start of a string buffer where the string is stored
@ len	– length of the string that is stored in the buffer (in bytes)
Return value:
“int ” – returns integer representing the number of bytes written to the socket
Example:
bytesWritten = pico_socket_write(sk_tcp, buf, bufLength);

The pico_socket_sendto function
Description:
This function is be called by the “pico_socket_write” and “pico_socket_send” functions. This function sends a string from the local address to the remote address, without checking if the remote is connected or not.
Function prototype:
int pico_socket_sendto(struct pico_socket *s, void *buf, int len, void *dst, uint16_t remote_port);

Parameters:
@ s	– pointer to socket of type “struct pico_socket”
@ buf	– void pointer to the start of a string buffer where the string is stored
@ len	– length of the string that is stored in the buffer (in bytes)
Return value:
“int ” – returns integer representing the number of bytes written to the socket
Example:
bytesWritten = pico_socket_sendto(sk_tcp, buf, len, &sk_tcp->remote_addr, sk_tcp->remote_port);

The pico_socket_recvfrom function
Description:
This function is called to receive a string of data from the specified socket. This function also checks if the socket is bound but not if it is connected or shutdown locally.
Function prototype:
int pico_socket_recvfrom(struct pico_socket *s, void *buf, int len, void *orig, uint16_t *remote_port);
Parameters:
@ s	– Pointer to socket of type “struct pico_socket”
@ buf	– Void pointer to the start of a string buffer where the string will be stored
@ len	– Length of the string that will be stored in the buffer (in bytes)
@ orig	– Pointer to the origin of the IPv4/IPv6 frame header
@ remote_port	– Portnumber of the sender socket
Return value:
“int ” – returns integer representing the number of bytes read from the socket
Example:
 bytesRcvd = pico_socket_recvfrom(sk_tcp, buf, bufLen, &peer, &port);

The pico_socket_send function
Description:
This function is called to send a string of data to the specified socket. This function also checks if the socket is connected and then calls the pico_socket_sendto function.
Function prototype:
int pico_socket_send(struct pico_socket *s, void *buf, int len);
Parameters:
@ s	– Pointer to socket of type “struct pico_socket”
@ buf	– Void pointer to the start of a string buffer where the string is stored
@ len	– Length of the string that is stored in the buffer (in bytes)
Return value:
“int ” – returns integer representing the number of bytes written to the socket
Example:
bytesRcvd = pico_socket_send(sk_tcp, buf, bufLen);

The pico_socket_recv function
Description:
This function directly calls the pico_socket_recvfrom function
Function prototype:
int pico_socket_recv(struct pico_socket *s, void *buf, int len);
Parameters:
@ s	– Pointer to socket of type “struct pico_socket”
@ buf	– Void pointer to the start of a string buffer where the string will be stored
@ len	– Length of the string in the socket buffer (in bytes)
Return value:
“int ” – returns integer representing the number of bytes read from the socket
Example:
bytesRcvd = pico_socket_recv(sk_tcp, buf, bufLen);
The pico_socket_bind function
Description:
This function binds a local IP-address and port to the specified socket.
Function prototype:
int pico_socket_bind(struct pico_socket *s, void *local_addr, uint16_t *port);
Parameters:
@ s	– Pointer to socket of type “struct pico_socket”
@ local_addr	– Void pointer to the local IP-address
@ port	– Local portnumber to bind with the socket
Return value:
“int ” – returns integer representing an error message
→ -1	=> Error : missing arguments
→ 0	=> Bind succesfull
Example:
errMsg = pico_socket_bind(sk_tcp, &sockaddr4→addr, &sockaddr4→port);

The pico_socket_connect function
Description:
This function connects a local socket to a remote socket of a server that is listening.
Function prototype:
int pico_socket_connect(struct pico_socket *s, void *srv_addr, uint16_t remote_port);
Parameters:
@ s	– Pointer to socket of type “struct pico_socket”
@ srv_addr	– Void pointer to the remote IP-address to connect to
@ remote_port	– Remote port number on which the socket will be connected to
Return value:
“int ” – returns integer representing an error message
→ -1	=> error available in pico_err
→ 0	=> Conncet succesfull
Example:
errMsg = pico_socket_connect(sk_tcp, &sockaddr4->addr, sockaddr4->port);

The pico_socket_listen function
Description:
A server can use this function when a socket is opened and bound to start listening to it.
Function prototype:
int pico_socket_listen(struct pico_socket *s, int backlog);
Parameters:
@ s	– Pointer to socket of type “struct pico_socket”
@ backlog	–
Return value:
“int ” – returns integer representing an error message
→ -1	=> Error available in pico_err
→ 0	=> Listening started succesful
Example:
errMsg = pico_socket_listen(sk_tcp, 3);

The pico_socket_accept function
Description:
When a server is listening on a socket and the client is trying to connect. The server on his side will wakeup and acknowlegde the connection by calling the this function.

Function prototype:
struct pico_socket *pico_socket_accept(struct pico_socket *s, void *orig, uint16_t *local_port);

Parameters:
@ s	– Pointer to socket of type “struct pico_socket”
@ orig	– Pointer to the origin of the IPv4/IPv6 frame header
@ local_port	–

Return value:
“struct pico_socket ” – The pointer to a pico_socket that represents the client thas was just connected

Example:
client = pico_socket_accept(sk_tcp, &peer, &port);

The pico_socket_shutdown function
Description:
Used by the pico_socket_close function to shutdown read and write mode for the specified socket. With this function one can close a socket for read and/or writting.

Function prototype:
int pico_socket_shutdown(struct pico_socket *s, int mode);

Parameters:
@ s	– Pointer to socket of type “struct pico_socket”
@ mode	– PICO_SHUT_RDWR, PICO_SHUT_WR, PICO_SHUT_RD

Return value:
“int ” – returns integer representing an error message
→ -1	=> Error available in pico_err
→ 0	=> socket shutdown succesful

Example:
errMsg = pico_socket_shutdown(s, PICO_SHUT_RDWR);

The pico_socket_close function
Description:
Function used on application level to close a socket. Always closes read and write connection.

Function prototype:
int pico_socket_close(struct pico_socket *s);

Parameters:
@ s	– Pointer to socket of type “struct pico_socket”

Return value:
“int ” – returns integer representing an error message
→ -1	=> Error available in pico_err
→ 0	=> socket shutdown succesful

Example:
errMsg = pico_socket_close(sk_tcp);